## Slide 1: Chapter 2 Wireless Data Transmission
Reference: Jorge Olenewa, Guide to Wireless Communications, 3rd edition, ISBN-13: 9781111307318, 2013
© Cengage Learning 2014
Department of Computer Engineering, Faculty of Engineering Prince of Songkla University, Phuket Campus

## Slide 2: Objectives
Discuss the two types of wireless transmissions
Explain the properties of a wave, such as amplitude, wavelength, frequency, and phase
Describe the basic concepts and techniques related to the transmission of data by radio waves

## Slide 3: Wireless Signals
Data travel in the “air”?
  Can data send in the outer space (outside world)?
Wireless data signals travel on electromagnetic waves
  Through space at the speed of light
    300,000 kilometers per second
Two basic types of waves
  Infrared light
  Radio waves

## Slide 4
Figure 2-1 Electromagnetic spectrum

## Slide 5: Wireless Signals
Two basic types of waves
  Infrared Light
  Radio Waves

## Slide 6: Infrared Light
Infrared (IR) light is electromagnetic radiation with longer wavelengths than those of visible light.
This range of wavelengths corresponds to a frequency range of approximately 430 THz down to 300 GHz.
The existence of infrared radiation was first discovered in 1800 by astronomer William Herschel.

## Slide 7: Infrared Light for Communications
It is easy to transmit information with light
  Light has two properties: off and on
  A 1 in binary code could result in a light quickly flashing on; a 0 could result in the absence of light
Light spectrum
  Types of light that travel from the Sun to the Earth
Infrared light
  Adjacent to visible light (although invisible)
  A much better medium for data transmission
  Less susceptible to interference

## Slide 8
Figure 2-2 Transmitting a message using visible light

## Slide 9: Infrared Light for Communications
Infrared wireless systems require:
  Emitter that transmits a signal (LED)
  Detector that receives the signal
Infrared wireless systems send data by the intensity of the light wave
  Detector senses the higher intensity pulse of light
    And produces a proportional electrical current
Infrared wireless transmission types
  Directed transmission (called line-of-sight or LOS)
  Diffused transmission – relies on reflected light

## Slide 10
Figure 2-3 Light pulses

## Slide 11
Figure 2-4 Directed infrared transmission

## Slide 12
Figure 2-5 Diffused infrared transmission

## Slide 13: Infrared Light
Advantages
  It does not interfere with other types of communication signals
  It is not affected by other signals (except light)
  Infrared light does not penetrate walls
    Signals are kept inside a room
Limitations
  Lack of mobility
  Range of coverage
    Can cover a range of only 50 feet (15 meters)
    Diffused infrared can only be used indoors
  Speed of transmission

## Slide 14: Infrared Light
Some specialized wireless local area networks are based on the infrared method
  Used in situations where radio signals would interfere with other equipment
Light waves cannot penetrate through materials like wood or concrete
  Heat rays are absorbed by most objects
  Solid objects, dust and humidity can limit the distance that light and infrared waves can travel

## Slide 15: Radio Waves
Radio waves are a type of electromagnetic radiation with wavelengths in the electromagnetic spectrum longer than infrared light.
Radio waves have frequencies from 300 GHz to as low as 3 kHz.
Like all other electromagnetic waves, they travel at the speed of light.

## Slide 16: Radio Waves
Naturally occurring radio waves are made by lightning, or by astronomical objects.
Artificially generated radio waves are used for fixed and mobile radio communication:
  Broadcasting, radar and other navigation systems, communications satellites, computer networks and innumerable other applications.

## Slide 17: Radio Waves
Different frequencies of radio waves have different propagation characteristics in the Earth's atmosphere.
  Shortwave radio (shortwave frequency) can reflect off the ionosphere and travel around the world, and much shorter wavelengths bend or reflect very little and travel on a line of sight e.g., AM radio.
  Longwave radio may cover a part of the Earth very consistently e.g., FM radio.
Notes: Shortwave radio refers to radio transmissions using shortwave frequencies.!!!

## Slide 18: Radio Waves
AM Radio vs. FM Radio
  AM: 535 to 1705kHz
  FM: 88 to 108 MHz

## Slide 19: Radio Waves
Radio waves provide the most common and effective means of wireless communications today
  Energy travels through space or air in electromagnetic waves
Antenna
  Length of copper wire, or similar material with one end free and the other end connected to a receiver or transmitter
Notes: Many people use radio wave for communication (majority)
Energy (data) travel in the air in electromagnetic
Radio wave come from: Electric current  wire  Create magnetic field (around wire)
Magnetic field move  Create radio wave (move out)

## Slide 20: Radio Waves
Electrical current moves the antenna
  At the same frequency as the radio waves
Electromagnetic wave (EM wave) – continuous (analog) combination of magnetism and electrical pressure (voltage) moving away from an antenna
Radio (radiotelephony) waves
  When an electric current passes through a wire, it creates a magnetic field
    In the space around the wire
  As this magnetic field radiates or moves out, it creates radio waves

## Slide 21: Frequency and Wavelength
A magnetic field and an electrical field around the antenna.
Receiver antenna can pickup transmitted radio signals

## Slide 22
Figure 2-18 Radio antennas transmitting and receiving signals

## Slide 23: Radio Waves
Advantages of radio waves
  Can travel great distances
  Can penetrate most solid objects
    With the exception of metallic ones
  Invisible
Figure 2-9 Radio waves can
penetrate most solid objects

## Slide 24: How Radio Data is Transmitted
Radio waves can be used to transmit data
  Over long distances
  Without the need for wires
Types of data
  Analog data
  Digital data

## Slide 25: Analog and Digital
Analog signal
  The intensity of the waves (voltage or amplitude) varies
  It is broadcast continuously
  Examples:
    Audio, video, voice, and light
Figure 2-10 Analog signal

## Slide 26: Analog and Digital
Digital signal
  Consists of discrete or separate pulses
  Has numerous starts and stops throughout the signal stream
Computers operate using digital signals
  Analog signal must be converted into a digital format
    Before it can be stored and processed or interpreted by a computer

## Slide 27
Figure 2-11 Simulating a digital signal with a garden hose
Figure 2-12 Digital signal

## Slide 28: Analog and Digital
To transmit a digital signal over an analog medium, a modem is used
  Modem (Modulator/Demodulator)
    Converts the distinct digital signals from a computer
    Encodes them into a continuous analog signal
      For transmission over analog phone lines
Modulation
  Process of encoding the digital signals (bits) onto an analog wave

## Slide 29: Frequency and Wavelength
Wavelength – distance between any point in one wave cycle and the same point in the next wave cycle
Frequency – Rate at which a radio circuit creates the waves
  The number of times a cycle occurs within one second
Carrier signal
  Sent by radio transmitters
  Continuous wave (CW) of constant amplitude (also called voltage) and frequency
  An up-and-down wave called an oscillating signal or a sine wave

## Slide 30
Figure 2-15 Sine wave (analog wave) and frequency

## Slide 31: Frequency and Wavelength
A change in voltage does not create a change in frequency
The term Hertz (Hz) is used to measure frequency
  A Kilohertz (KHz) is 1,000 Hertz
  A Megahertz (MHz) is 1,000,000 Hertz
  A Gigahertz (GHz) is 1,000,000,000 Hertz
The wave measured as 710,000 Hz is referred to as 710 KHz

## Slide 32
Figure 2-16 Two different frequencies; same amplitude

## Slide 33: Transmission Speed
Speed of transmission is usually shown in bits per second (bps)
Baud rate
  Another term used in measuring the speed of radio transmission
  Number of signal units per second that are required to represent the bits transmitted
  Baud is a change in the carrier signal
It is possible to have a change in signal (a baud) represent more than 1 bit

## Slide 34
Table 2-2 Bit representation of four signal changes

## Slide 35: Transmission Speed
Analog modems transmit at a rate of 4,800 baud
  Maximum number of signal changes per second that a phone line can support
Current modems can transmit up to 33,600 bps
  Using more complex modulation techniques
    Along with compression of the data
When a signal unit can represent:
  Two bits, it is known as a dibit
  Three bits, it is known as a tribit
  Four bits, it is known as a quadbit
Notes: 4800 baudx 7 bit = 33,600 bps

## Slide 36: Transmission Speed
Bandwidth
  Range of frequencies that can be transmitted by a particular system or medium
  Refers to the maximum data transmission capacity
  Accurate only when referring to purely digital systems

## Slide 37: Analog Modulation
Representation of analog information by an analog signal
Analog modulation types
  Amplitude modulation
  Frequency modulation
  Phase modulation
Amplitude modulation (AM)
  Height of a carrier wave is known as the amplitude
    Can be measured in volts (electrical pressure)
  Height of the carrier wave is changed in accordance with the height of the modulating signal

## Slide 38
Figure 2-19 Amplitude of a signal

## Slide 39: Analog Modulation
Amplitude modulation (AM)
  Used by broadcast radio stations
  Very susceptible to interference from outside sources
Frequency modulation (FM)
  Number of waves that occur in one second undergoes change based on the amplitude of the modulating signal
  Often used by broadcast radio stations
  Not as susceptible to interference from outside sources
  FM carrier has a wider bandwidth
    Allows it to carry Hi-Fi as well as stereophonic signals

## Slide 40
Figure 2-21 Frequency modulation (FM)

## Slide 41: Analog Modulation
Phase modulation (PM)
  Changes the starting point of the cycle
  It is not generally used to represent analog signals
  A signal composed of sine waves has a phase associated with it
  Phase is measured in degrees
    One complete wave cycle covers 360 degrees
  A phase change is always measured with reference to some other signal
  PM systems almost always use the previous wave cycle as the reference signal

## Slide 42
Figure 2-22 Visual representation of phase shift

## Slide 43: Digital Modulation
Method of encoding a digital signal onto an analog wave
  For transmission over a medium that does not support digital signals
In a digital system, the changes are distinct using binary signals
  Which exist in one of two states, a 1 or a 0
For a computer to be able to understand these signals
  Each bit must have a fixed duration to represent 1 or 0

## Slide 44: Digital Modulation
Advantages
  Makes better use of the bandwidth available
  Requires less power to transmit
  Performs better when the signal experiences interference from other signals
  Error-correcting techniques are more compatible with other digital systems
There are three basic types of digital modulations:
  Amplitude, frequency, and phase
Users demand more transmission speed
  Today there are dozens of different types of modulation

## Slide 45: Digital Modulation
Binary signals
  Digital data transmissions are typically sent in bursts of bits
  Three types of binary signaling techniques can be used:
    Return-to-zero (RZ)
    Non-return-to-zero (NRZ)
    Polar non-return-to-zero (polar NRZ)
      Also known as non-return-to-zero-level (NRZ-L)
  A variation of NRZ-L is non-return-to-zero, invert-on-ones (NRZ-I)

## Slide 46
Figure 2-23 Return-to-zero (RZ)

## Slide 47
Figure 2-24 Non-return-to-zero (NRZ)

## Slide 48
Figure 2-25 Polar non-return-to-zero (non-return-to-zero level or NRZ-L)

## Slide 49
Figure 2-26 Non-return-to-zero, invert-on-ones (NRZ-I)

## Slide 50: Digital Modulation
Amplitude Shift Keying (ASK)
  Binary modulation technique similar to amplitude modulation
  Height of the carrier signal can be changed to represent a 1 bit or a 0 bit
  ASK uses NRZ coding
Frequency Shift Keying (FSK)
  Binary modulation technique that changes the frequency of the carrier signal
  More wave cycles are needed to represent a 1 bit

## Slide 51
Figure 2-27 Amplitude shift keying (ASK)

## Slide 52
Figure 2-28 Frequency shift keying (FSK)

## Slide 53: Digital Modulation
Phase Shift Keying (PSK)
  Binary modulation technique similar to phase modulation
  Transmitter varies the starting point of the wave
  PSK signal starts and stops because it is a binary signal
  Quadrature amplitude modulation (QAM)
    Technique of combining amplitude and phase modulation
  Receivers can detect phase changes much more reliably than a frequency or amplitude change
    In the presence of electromagnetic noise

## Slide 54
Figure 2-29 Phase shift keying (PSK)

## Slide 55
Figure 2-30 Phase modulation angles

## Slide 56: Digital Modulation
Binary phase shift keying (BPSK)
  Can be used to transmit dibits (four signal changes equals 2 bits per signal change)
Figure 2-32 Transmitting dibits using BPSK
Notes: Phase is referenced by a previous wave

## Slide 57: Spread Spectrum
Narrow-band transmissions
  Each signal transmits on one radio frequency
    Or a very narrow range of frequencies
  Vulnerable to outside interference from another signal
  Radio signal transmissions are narrow-band
Spread spectrum transmission
  Takes a narrow band signal and spreads it over a broader portion of the radio frequency band
  Results in less interference and fewer errors
  Two common methods
    Frequency hopping and direct sequence

## Slide 58
Figure 2-33 Spread spectrum vs. narrow-band transmission

## Slide 59: Frequency Hopping Spread Spectrum (FHSS)
Uses a range of frequencies
  Changes frequencies several times during transmission
Hopping code
  The sequence of changing frequencies
  The receiving station must also know the hopping code
  Multiple radios can each use a different sequence of frequencies within the same area
    And never interfere with each other
If interference is encountered on a frequency
  Only a small part of the message is lost

## Slide 60
Figure 2-34 Frequency hopping spread spectrum (FHSS) transmission

## Slide 61
Figure 2-35 FHSS error detection

## Slide 62: Frequency Hopping Spread Spectrum (FHSS)
Frequency hopping can reduce the impact of interference from other radio signals
An interfering signal will affect the FHSS signal only when both are transmitting at the same frequency and at the same time
  Because FHSS transmits short bursts over a wide range of frequencies, the extent of any interference will be small
    The error can be detected through error checking
    Message can be easily retransmitted

## Slide 63: Direct Sequence Spread Spectrum (DSSS)
Similar as: Word spelling when communicate by telephone (Somchai: Singapore, Oxygen, Man…)
Uses an expanded redundant code to transmit each data bit
  And then a modulation technique such as QPSK
  A DSSS signal is effectively modulated twice
Barker code (or chipping code)
  A particular sequence of 1s and 0s
  Ideal for modulating radio waves
    As well as for being detected correctly by the receiver
  It is also called a pseudo-random code
Before transmission, add the original data bit to the chipping code

## Slide 64
Figure 2-36 Encoding before modulation in a DSSS transmission

## Slide 65: Direct Sequence Spread Spectrum (DSSS)
DSSS system transmits combinations of multiple chips
  11 chips are transmitted at a rate 11 times faster than the data rate
Characteristics
  Frequency of the digital component of the signal is much higher than that of the original data (chip rate)
  A plot of the frequency spectrum of this signal would look similar to random noise
  All of the information contained in the original signal (a 0 or a 1 bit) is still there!

## Slide 66
Figure 2-37 Spreading the signal over a wider range of frequencies

## Slide 67: Direct Sequence Spread Spectrum (DSSS)
Advantages
  DSSS signal appears to an unintended narrow-band receiver to be low-powered noise
  Noise can cause some of the chips to change value
    Receiver can recover the original data bit
      Using statistical techniques and mathematical algorithms
      Thus avoiding the need for retransmission
DSSS devices are typically higher-end products
  Because they are more expensive to manufacture than FHSS systems

## Slide 68: Summary
American Standard Code for Information Interchange (ASCII)
  Coding scheme that uses numbers from 0 to 127 to represent symbols
Wireless transmissions do not use wires or any other visible media
Infrared wireless transmission can be either directed or diffused
Radio transmissions use a carrier signal
  A continuous wave (CW) of constant amplitude (voltage) and frequency

## Slide 69: Summary
Carrier signal can undergo three types of modulation:
  Amplitude, frequency, and phase
Digital modulation basic techniques
  Amplitude, frequency and phase
Radio signals are by nature a narrow-band type of transmission
  Transmit on one radio frequency or a very narrow spectrum of frequencies

## Slide 70: Summary
Spread spectrum
  Takes a narrow signal and spreads it over a broader portion of the radio frequency band
Spread spectrum common methods
  Frequency hopping spread spectrum (FHSS)
  Direct sequence spread spectrum (DSSS)

## Slide 71: Homework
Prepare to send your name to network
  Write your name in English and translate to hexadecimal (e.g., Bob => 42-6F-62)
    Using ASCII Table
  Convert hexadecimal value of your name to binary
    Put group of 8 bits together
Draw a wave form to show a digital signal of your name
  Using Amplitude Shift Keying (ASK)
  Using Frequency Shift Keying (FSK)
  Using Binary Phase Shift Keying (BPSK)