## Slide 1: Chapter 3 Radio frequency communication
Reference: Jorge Olenewa, Guide to Wireless Communications, 3rd edition, ISBN-13: 9781111307318, 2013
© Cengage Learning 2014
Department of Computer Engineering, Faculty of Engineering Prince of Songkla University, Phuket Campus

## Slide 2: Objectives
List the components of a radio system
Describe the factors that affect the design of a radio system
Discuss why standards are beneficial and list the major telecommunications standards organizations
Explain the radio frequency spectrum

## Slide 3: Components of a Radio System
Components include:
  Filters
  Mixers
  Amplifiers
  Antennas

## Slide 4: Filters
Filter: removes unwanted RF signals
RF filter
  Either passes or rejects a signal based on frequency
Types of filters
  Low-pass filter: maximum frequency is set and all signals below that value are allowed
  High-pass filter: minimum frequency is set and all signals above that level are allowed
  Bandpass filter: sets a range called a passband and signals that fall within the passband are allowed

## Slide 5
Figure 3-2 Low-pass filter
Figure 3-3 High-pass filter
Figure 3-4 Bandpass filter

## Slide 6: Filters
Filters are also found in transmitters
  Used to eliminate some unwanted frequencies called harmonic oscillations
    Result from the process of modulating the signal before transmission
Intermediate frequency (IF) signal
  Resulting output from the modulation process
IF signal is filtered through a bandpass filter
  To remove any undesired high- or low-frequency signals

## Slide 7
Figure 3-5 Filter function in a radio transmitter

## Slide 8: Mixers
Mixers: combine two radio frequency inputs to create a single output
  Output is in the range of the highest sum and the lowest difference of the two frequencies
  Sum and differences are known as the sidebands of the frequency carrier
    Shield transmitted signal from “stray” signals
Used to convert an input frequency to a specific desired output frequency

## Slide 9
Figure 3-6 Mixer symbol
Figure 3-7 Mixer output

## Slide 10
Figure 3-8 AM radio sidebands

## Slide 11: Amplifiers
Amplifiers: increase the amplitude of an RF signal
RF signals tend to lose intensity (amplitude)
  When they move through circuits, air, or space
Amplifier is an active device
  Must be supplied with electricity
  Uses this electricity to increase a signal’s intensity or strength
    Then output an exact copy of the input signal with a higher amplitude

## Slide 12: Antennas
Antennas: transmit or receive an RF signal
  Antennas will be discussed in greater detail in Chapter 4
Figure 3-11 Antenna symbol

## Slide 13: Radio system components
Table 3-1 Radio system components and their symbols

## Slide 14: Design of a Radio System
Designers of radio communications systems
  Need to consider how the systems will be used
    Signal broadcasting
      E.g., size and location of antenna, coverage area
  Other considerations:
    Multiple user access
    Transmission direction
    Switching and Signal strength

## Slide 15: Multiple Access
Only a limited number of frequencies are available for radio transmission
  Conserving the use of frequencies is important
Conserving a frequency
  Share a frequency among multiple users
Methods that allow multiple access
  Frequency Division Multiple Access (FDMA)
  Time Division Multiple Access (TDMA)
  Code Division Multiple Access (CDMA)

## Slide 16
Figure 3-12 Multiple access

## Slide 17: Multiple Access
Frequency Division Multiple Access (FDMA)
  Divides the bandwidth of a channel into several smaller frequencies bands
  Most often used with analog transmissions
  Cable television is transmitted using FDMA
  Drawback of FDMA: Crosstalk
    Causes interference on the other frequency and may disrupt the transmission

## Slide 18
Figure 3-13 Frequency Division Multiple Access (FDMA)

## Slide 19: Multiple Access
Time Division Multiple Access (TDMA)
  Divides the transmission time into several slots
  Each user is assigned the entire frequency for the transmission
    For a fraction of time on a fixed, rotating basis
  Advantages
    Uses the bandwidth more efficiently
    Allows both data and voice transmissions to be mixed using the same frequency

## Slide 20
Figure 3-14 Time Division Multiple Access (TDMA)

## Slide 21: Multiple Access
Code Division Multiple Access (CDMA)
  Used primarily for cellular telephone communications
  Uses direct sequence spread spectrum (DSSS)
    With a unique digital spreading code (PN code)
  Before transmission occurs
    High-rate PN code is combined with the data to be sent
      Spreads the signal over a wide frequency band
  The longer the code is, the more users will be able to share the same channel
  Number of chips in the code
    Determines the amount of spreading or bandwidth

## Slide 22: Multiple Access
Figure 3-15 CDMA spreading of a data signal by a PN code

## Slide 23: Multiple Access
Code Division Multiple Access (cont’d)
  Spreading process is reversed at the receiver
    Code is de-spread to extract the original data bit transmitted
Figure 3-16 De-spreading a CDMA signal to recover the data bits

## Slide 24: Multiple Access
Figure 3-17 Attempting to de-spread another receiver’s CDMA signal

## Slide 25: Multiple Access
PN Code as a language
  A room with 20 people, 10 simultaneous 1-1 conversation
  All pairs are talking at the same time with different languages
  Ignore noise level issue in the room
  Other 9 conversations don’t bother them since none of the listeners understands any other languages

## Slide 26: Multiple Access
Code Division Multiple Access (cont’d)
  Advantages
    Can carry up to three times the amount of data as TDMA
    Transmissions are much harder to eavesdrop on
    A would-be eavesdropper must also know the exact chip in which the transmission starts

## Slide 27: Transmission Direction
Simplex transmission
  Occurs in only one direction
  Rarely used in wireless communication today
    Except for broadcast radio and television
Half-duplex transmission
  Sends data in both directions
    But only one way at a time
  Used in consumer devices such as citizens band (CB) radios or walkie-talkies
    User must hold down the “talk” button while speaking

## Slide 28
Figure 3-18 Simplex transmission

## Slide 29
Figure 3-19 Half-duplex transmission

## Slide 30: Transmission Direction
Full-duplex transmission
  Allows data to flow in both directions simultaneously
  Example: A telephone system
  If the same antenna is used for wireless transmission and reception
    A filter can be used to handle full-duplex transmissions
  Full-duplex wireless communications equipment
    Sends and receives on different frequencies

## Slide 31
Figure 3-20 Full-duplex transmission
Figure 3-21 Using a single antenna in full-duplex RF communications

## Slide 32: Switching
Why we need switching?
6 telephones require 5 cables to connect to all the others.
Thus, total = 15 needed cables.
Mesh network:
n(n-1)/2 (n = number of devices)
3 telephones require 2 cables to connect to all the others.
Thus, total = 3 needed cables.

## Slide 33: Switching
Involves moving the signal from one wire or frequency to another
Circuit switching
  Type of switching used by telephone systems
  A dedicated and direct physical connection is made between the caller and the recipient
    Direct connection lasts until the end of the call
Packet switching
  Used by data networks
  Data transmissions are broken into packets
  Each packet is sent independently

## Slide 34
Figure 3-22 Telephone call switching

## Slide 35
Figure 3-23 Packet switching

## Slide 36: Switching
Packet switching advantages
  Allows better utilization of the network
  Allows multiple computers to share the same line or frequency
  If a transmission error occurs
    It usually affects only one or a few packets
    Only packets affected must be resent, not entire message

## Slide 37: Signal Strength
Strength of the signal in a radio system
  Must be sufficient for the signal to reach its destination
    With enough amplitude to be picked up by the antenna
    And for the information to be extracted from it
Electromagnetic interference (EMI)
  Affects radio signal strength
  Also called noise
Signal-to-noise ratio (SNR)
  Compares signal strength with background noise
  When strength of a signal is well above the noise, interference can be filtered out

## Slide 38
Figure 3-24 Sources of EMI or noise (interference)

## Slide 39
Figure 3-25 Signal-to-noise ratio (SNR)

## Slide 41: Signal Strength
The power of a signal is 10 mW and the power of the noise is 1 μW; what are the values of SNR and SNRdB ?
Solution
  The values of SNR and SNRdB can be calculated as follows:

## Slide 42: Signal Strength
To reduce the interference of noise
  Boost the strength of the signal
  Use of filters on the receiving end
Attenuation
  A loss of signal strength
Multipath distortion
  As a radio signal is transmitted, the electromagnetic waves spread out
  Waves travel different paths between transmitter and receiver
    Arrive at different times and out of phase

## Slide 43
Figure 3-26 Multipath interference or distortion

## Slide 44
Figure 3-27 Effect of multipath distortion in a signal

## Slide 45: Signal Strength
Directional antenna
  Used to minimize multipath distortion
  Radiates electromagnetic waves in one direction only
Other methods to reduce multipath distortion
  Use an amplifier in front of receiver to increase SNR
  Transmit the same signal on separate frequencies

## Slide 46: Understanding Standards
Standards for telecommunications have been in place almost since the beginning of the industry
  Standards have played an important role in the rapid growth of the industry

## Slide 47: The Need For Standards
Standards
  Commonly accepted technical specifications
Telecommunications requires standards exist for the design, implementation, and operation of the equipment
A lack of standards between devices would prevent communications from taking place

## Slide 48: Advantages and Disadvantages of Standards
Advantages
  Guarantee device interoperability
  Create competition
    Competition results in lower costs for consumers and improvements in products
    Competition also results in lower costs for manufacturers
  Help consumers protect their investment in equipment
Disadvantages
  Can be a threat to industries in large countries
    More overhead cost of products
  Although standards are intended to create unity
    They can have the opposite effect
      Political reasons to reject the standard and create its own
Notes: Threat => large countries has more overhead cost of products
Opposite effect => political to reject some standard => industry political

## Slide 49: Types of Standards
De Facto Standards
  Not official standards
  Common practices that industry follows
    E.g., M$ Windows has become the de facto standard for PC
De jure Standards
  Also called official standards
    E.g., Request For Comments (RFC)
  Controlled by an organization or body
    Published to members (individuals, companies)
  Process for creating standards can be very involved
Notes: De facto: e.g., M$ Windows has become the de facto standard for PC
De jure: RFC => published members (individual, company) who interested in the field => review, comment and revise before final draft (vote)

## Slide 50: Types of Standards
Why Consortia?
  De jure standard takes too long time to complete
    E.g., WLAN took 7 years while products are released long before the standard
Consortia
  Industry-sponsored organizations that promote a specific technology
  Not open to everyone, instead, specific high-profile companies create and serve on consortia
    E.g., W3C: M$, Netscape, Sun and IBM
      HTML, CSS, DOM
Notes: De jure is too long (e.g, WLAN = 7 yrs) , product is released long before the standard => Consortia: industry-sponsored

## Slide 51: Telecommunications Standards Organizations
United States Standards Groups
  American National Standards Institute (ANSI)
  Telecommunications Industries Association (TIA)
  Internet Engineering Task Force (IETF)
  Internet Architecture Board (IAB)
  Internet Society (ISOC)
  Institute of Electrical and Electronics Engineers (IEEE)

## Slide 52: Telecommunications Standards Organizations
Multinational Standards Groups
  European Telecommunications Standards Institute (ETSI)
International Standards Groups
  International Telecommunications Union (ITU)
  International Organization for Standardization (ISO)

## Slide 53: Regulatory Agencies
Enforcing telecommunications regulations is important
    E.g., Nobody buys cellular phones that refuses transmission standards
Regulations must be enforced by an outside agency
  Ensure all participants adhere to the prescribed standards
Federal Communications Commission (FCC)
  Primary regulatory agency for telecommunications in the United States
  Responsibilities
    Processes applications for licenses and other filings
    Analyzes complaints and conducts investigations
    Regulates radio and television broadcast stations
Notes: FCC and other country agencies continually monitor transmissions to ensure that no one is using a frequency without a license or is transmitting with more power than their license allows.

## Slide 54: Radio Frequency Spectrum
Radio frequency spectrum
  Entire range of all radio frequencies that exist
  Range extends from 10 KHz to over 30 GHz
  Spectrum is divided into 450 different sections (bands)
Radio frequencies of common devices include:
  Garage door openers, alarm systems: 40 MHz
  Baby monitors: 49 MHz
  Radio-controlled airplanes: 72 MHz
  Radio-controlled cars: 75 MHz
  Wildlife tracking collars: 215 MHz–220 MHz
  Global positioning system: 1.227 GHz and 1.575 GHz

## Slide 55
Table 3-3 Radio frequency bands

## Slide 56: Radio Frequency Spectrum
International spectrum allocations are established by the ITU
License exempt spectrum
  Unregulated bands
    Radio spectra available without charge to any users without a license
  Devices from different vendors may attempt to use the same frequency (disadvantage)

## Slide 57
Table 3-4 Unregulated bands

## Slide 58: Summary
Radio frequency system hardware components
  Filters, mixers, amplifiers, and antennas
Filter is used either to accept or block a radio frequency signal
Mixer combines two inputs to create a single output
Amplifier increases a signal’s intensity or strength
Multiple access methods
  FDMA
  TDMA
  CDMA

## Slide 59: Summary
Types of data flow
  Simplex
  Half-duplex
  Full-duplex
Switching involves moving the signal from one wire or frequency to another
Electromagnetic interference (EMI) is sometimes called noise
  Signal-to-noise ratio (SNR)
    Measure of signal strength relative to background noise

## Slide 60: Summary
Standards for telecommunications
  In place almost since the beginning of the industry
Radio frequency spectrum
  The entire range of all radio frequencies that exist

## Slide 61: Homework (CDMA)
Prepare to send your name to network
  Write your name in English and translate to hexadecimal (e.g., Bob => 42-6F-62)
    Using ASCII Table
  Convert hexadecimal value of your name to binary
    Put group of 8 bits together (choose only 1 character (8 bits))
Draw a wave form to show a digital signal of your name using CDMA
    Choose PN Code (Chipping code) to be any code by yourself
      PN Code must not the same in this example and has noise resistance
    Demonstrate ‘Encode’ and ‘Decode’ original data