## Slide 1: Chapter 4 HOW antennas work
Reference: Jorge Olenewa, Guide to Wireless Communications, 3rd edition, ISBN-13: 9781111307318, 2013
© Cengage Learning 2014
Department of Computer Engineering, Faculty of Engineering Prince of Songkla University, Phuket Campus

## Slide 2: Objectives
Define decibels, gain, and loss
Explain the purpose of an antenna
List the different antenna types, shapes and sizes as well as their applications
Explain RF signal strength and direction
Describe how antennas work

## Slide 3: Gain and Loss
Understanding RF signal transmission involves:
  The strength or the power with which the transmitter is sending the signal
  The amount of reduction in signal strength caused by cables, connectors, and other components
  The transmission medium (atmosphere or free-space)
  The minimum strength of the signal required by the receiver to be able to properly recover the data sent by the transmitter

## Slide 4: Gain and Loss
Amplifier boosts the power of a signal
  The effect is called a gain
Cables and connectors offer a resistance to the flow of electricity
  They tend to decrease the power of a signal (loss)
Signal power changes logarithmically
  Not in a linear fashion
Gain and loss are relative concepts
  Need to know the power level of the signal at two different points

## Slide 5
Figure 4-1 Linear vs. logarithmic

## Slide 6: Decibel
Decibel (dB)
  Ratio between two signal levels
  Makes it much simpler to express and calculate power gain or loss
Tens and threes of RF mathematics
  A gain of 3 dB (+3 dB) means the signal is two times bigger (twice the power)
  A gain of 10 dB (+10 dB) means the signal is 10 times bigger (10 times the power)
  The same applies for loss

## Slide 7: Decibel
Power (dB) = 10 log P2/P1
  where P2 and P1 are the power in watts
If P2/ P1 = 1 in watt, PdB = 10 log 1 dB = 0 dB
If PdB = 3, P2/ P1 = 2
If PdB = 10, P2/ P1 = 10 (10 = 10 log 1010)
3 = 10 log P2/P1 log P2/P1 = 0.3 P2/P1 = 100.3 = 2

## Slide 8: Decibel
Wireless device has output of 200 mW. It is connected to a cable with a 9 dB gain and a 6 dB loss. What is the effective device output power?
Gain in the cable = 9 dB
Loss in the cable = 6 dB
The net gain = 9 dB - 6dB = 3dB.
Notes: Effective Isotropic Radiate Power (EIRP) ใช้กำหนดว่า สุทธิ์แล้วสามารถส่งได้ไกลแค่ไหนที่ไม่ชนกับ ตัวส่งตัวอื่น ที่ความถี่ช่วงเดียวกัน
Active Gain = Transmitter amplifier (+dB) :
Passive Gain = Antenna focus (+dB)
Loss = Loss in cable, connector (-dB)
EIRP => Total dB = Effective Isotropic Radiated Power (output power: net gain)
For Unlicensed band (not mean uncontrol)
Max transmitter output power = 1 watt (for unlicensed, not mean uncontrol)
Max EIRP power = 4 watt

## Slide 9: Decibel
Every 3dB gain doubles the milliwatts.
As according to the popular "rule of 3's". Whenever losing or gaining by a factor of 3 dB, just divide or multiply by 2.
As device output power is 200 mw and we need to multiply it by a factor of 2 according to rule of 3
Output power = 400mW

## Slide 10: Decibel
Absolute power level of a signal is supplied by a transmitter, the strength of the output is +36 dBm. What is the output power in watts?
The absolute power signal is calculated as follow:
36 dBm = 10 dBm + 10 dBm + 10 dBm + 3 dBm + 3 dBm
Since 0 dBm = 1 mW
10 dBm => 10 mW (multiplied by 10)
x 2 of 10 dBm => 10mW x 102 = 1000 mW = 1 W
x 2 of 3 dBm => 1 W x 2 x 2 = 4 W
The output power in watts = 4 W.

## Slide 11: Decibel
dBm
  Relative way to indicate an absolute power level in the linear Watt scale
  1 mW = 0 dBm
Isotropic radiator
  Theoretically perfect sphere that radiates energy equally in all directions
    Not possible to build a real isotropic radiator since it needs a power source or signal cable connected to it at some point on the surface.
  Provides a reference point for representing the gain of an antenna
    A unit for the antenna gain compared to an isotropic radiator gain
    Usually expressed in dB isotropic (dBi)
The sun is the closest to an isotropic radiator
Notes: dBi => compare perfect sphere all directions radiator
dBd => compare dipole antenna (= 2.15 dBi)
Antenna 2 dBd = 2 dBi + 2.15 dBi = 4.15 dBi

## Slide 12: Decibel
For microwave and higher frequency antennas
  Gain is usually expressed in dB dipole (dBd)
  dBd is referred to a reference dipole antenna
Dipole
  The smallest, simplest, most practical type of antenna that can be made
    But that also exhibits the least amount of gain
  Has a fixed gain over that of an isotropic radiator of 2.15 dB
dipole antenna

## Slide 13
Table 4-1 Decibel values and references

## Slide 14: Antenna Characteristics
Characteristics of antennas
  Types
  Sizes
  Shapes
Notes: Antenna
  Length of copper wire, or similar material with one end free and the other end connected to a receiver or transmitter

## Slide 15: Antenna Types
Passive antennas
  The most common type
  Constructed of a piece of metal, wire, or similar conductive material
  Does not amplify the signal in any way
  Directional gain
    Passive antennas radiate the RF energy supplied by the transmitter in one direction
    Exhibits an effective gain that is similar to amplification of the signal

## Slide 16
Figure 4-2 Directional gain
Shapes of passive antennas radiate the RF energy in one direction called directional gain
Far distance
Wide area
Comparison RF signal as the light

## Slide 17: Antenna Types
Active antennas
  Passive antennas with an amplifier built-in
  Amplifier is connected directly to the piece of metal that forms the antenna itself
  Most active antennas have only one electrical connection
    RF signal and the power for the amplifier are supplied on the same conductor

## Slide 18: Antenna Sizes and Shapes
Size and shape of an antenna depend on:
  Frequency on which the antenna will transmit and receive
  Direction of the radiated electromagnetic wave
  Power with which the antenna must transmit
Antenna size is proportional to the wavelength it is designed to transmit or receive
Require larger antennas
  Lower frequency signals
  Higher gain

## Slide 19: Antenna Sizes and Shapes
Omnidirectional antennas
  Used to transmit and receive signals from all directions with relatively equal intensity
  Longer omnidirectional antennas usually have a higher gain

## Slide 20
High-gain omnidirectional antenna
omnidirectional antenna

## Slide 21: Antenna Sizes and Shapes
Directional antennas
  Transmit a signal in one direction only
  Yagi antenna emits a wider, less focused RF beam
  Parabolic dish antenna emits a narrow, more concentrated beam of RF energy

## Slide 22
Figure 4-5 Yagi antennas
Notes: Director element – รับสัญญาณคลื่นแม่เหล็กไฟฟ้า ชนกับ director element แรก ก็จะเหนี่ยวนำ คลื่นไฟฟ้า element ถัด ๆ (และเกิดสนามแม่เหล็กด้วย) ไป ให้ เกิดคลื่นไฟฟ้า ไปถึง Driven-dipole ยิ่งมี Director element มากยิ่ง รับสัญญาณได้ดีขึ้น ตัว Director element เป็นเสาบาง ๆ ไม่ต่อกับแผ่นวงจร คลื่นวิทยุ
Driven dipole – ต่อกับ วรจรวิทยุ แปลงจากสัญญาณไฟฟ้า เป็นข้อมูล TV
Reflector – สะท้อนคลื่นที่รับเข้ามา (เก็บตกสัญญาณที่เลยออกไป) ให้กับ Driven dipole
https://pantip.com/topic/33235199

## Slide 23
Parabolic dish antenna
Reflector
antenna

## Slide 24
DIY Parabolic antenna
http://www.usbwifi.orconhosting.net.nz/usbscoop.jpg

## Slide 25: Antenna Sizes and Shapes
Patch antennas
  Some are designed for installation on building walls
    To send an RF signal in one direction away from the structure
  One common application for patch antennas is in cellular telephony
Figure 4-7 Cellular antenna with cutout to show internal construction

## Slide 26
from: https://upload.wikimedia.org/wikipedia/commons/b/b3/Cell_phone_tower_disguised_2008.jpg

## Slide 27
Figure 4-8 Indoor patch antenna

## Slide 28: Signal Strength and Direction
Distance between the transmitter and receiver
  Determines the strength of the signal
Transmitters produce a finite amount of RF energy
  For most applications, active antennas can be extremely expensive
Omnidirectional antenna divides strength of signal in a 360-degree circle around the antenna
Free space loss
  RF waves tend to spread away from the source of the signal (the antenna)
  Free space loss calculator tools can be found on Internet

## Slide 29: Antenna Performance
Antenna performance
  A measure of how efficiently an antenna can radiate an RF signal
Design, installation, size, and type of antenna can affect its performance

## Slide 30: Radiation Patterns
Antenna pattern
  Graphic developed by measuring the signal radiating from the antenna
  Indicates the direction, width, and shape of the RF signal beam coming from the antenna
Antennas emit signals in two dimensions
  Horizontally and vertically
Antenna specifications almost always include the vertical beam angle that a particular antenna emits
Notes: Radiation pattern ของเสาอากาศ ใช้เพื่อ แสดงความแรงของคลื่นวิทยุในทิศทางต่าง ๆ โดยรอบสายอากาศ ที่ระยะห่างคงที่จากสายอากาศ

## Slide 31
Figure 4-9 Antenna patterns viewed from above
Notes: Omini
แผ่กระจายเท่ากันทุกทิศทาง
Yagi
minor lobe – พูคลื่นเล็ก (side lobes, back lobe)
Main lobe – พูคลื่นหลัก เป็นพูคลื่นที่มีความแรงมากที่สุด

## Slide 32
Figure 4-10 Vertical antenna pattern (side view of omnidirectional antenna pattern)

## Slide 33: Antenna Polarization
Antenna polarization: orientation of the wave leaving the antenna
Vertical polarization
  Sine waves travel up and down when leaving antenna
Horizontal polarization
  Sine waves travel from side to side on a horizontal plane
Most efficient signal transmission and reception is experienced when both antennas are equally polarized
Notes: Antenna polarization => it oscillates either horizontally or vertically

## Slide 34
Figure 4-11 Antenna polarization

## Slide 35
Figure 4-12 Mixed vertical and horizontal antenna polarizations

## Slide 36: Monopole and dipole antennas
Monopole antenna
  Basically a length of wire or metal
  Straight piece of wire or metal, with no reflecting or ground element
  One-dimensional antennas
Dipoles are commonly built as two monopoles
  Mounted together at the base
A monopole antenna is less efficient than a dipole
Figure 4-13 Common dipole antenna

## Slide 37: Smart Antennas
Used primarily in mobile or cellular telephony
“Learn” where the mobile receiver is
  Can track and focus RF energy in specific direction
Classes of smart antennas
  A switched beam antenna
    Uses several narrow beam antennas pointing in different directions
  Adaptive or phased array antennas
    Divided into a matrix of radiating elements
    Has the effect of sending the energy beam in a particular direction (generally called “beam forming”)
    Used extensively in ultramodern radar systems.

## Slide 38
Figure 4-15 Directional antenna vs. smart antenna

## Slide 39: Antenna System Implementation
Proper installation of antennas requires knowing the user’s requirements
Challenges
  Physical obstacles
  Other regulatory restrictions

## Slide 40: Antenna Cables
Most antennas are connected to the transmitter or receiver using coaxial cable
Impedance
  Represented by the letter “Z” and measured in ohms
  Cable’s impedance must match that of the transmitter circuit as well as that of the antenna
    Removable high-gain antenna may use a non-standard connector in order to protect the mismatch of transmitter EIRP assigned by FCC
You must consider the signal loss caused by the connector and by the cable itself
Notes: Antenna ที่ ถอดออกได้ จะต้องเป็นแบบ Non-standard connector ใช้กับ transmitter นั้น ๆ เท่านั้น เพื่อป้องกัน transmitter ที่ส่งกำลังส่งเกินกว่า EIRP ที่กำหนดโดย FCC
ผู้ใช้ สามารถซื้อ Transmitter โดยไม่มี Antenna ได้ แต่ตัว Antenna ที่กำลังสูง จะต้องไม่ใช่ standard connector

## Slide 41: Antenna Cables
Cable loss is measured in relation to the length of the cable
You can use special low-loss antenna cables to minimize signal loss
Table 4-2 Low-loss LMR cables
LMR coaxial is expensive more regular coaxial
Notes: 100 feet = 30.48 meters
10 feet (3 m.) => loss = 3.9 dB (LMR-100) => transmitter output loss > half of energy (before adding connector losses)
loss = 0.7 dB (LMR-400)
Thick cable => less loss

## Slide 42: RF Propagation
The way that radio waves propagate depends on the frequency of the signal
RF waves are classified in three groups:
  Ground waves follow the curvature of the earth
  Sky waves bounce between the ionosphere and the surface of the earth
  Line-of-sight used by RF waves transmitted in frequencies between 30 MHz and 300 GHz
    Require a line-of-sight path between the transmitter and the receiver antennas
Notes: Move between trans – recv through air/atmosphere

## Slide 43
Table 4-3 RF wave propagation groups
Figure 4-18 How radio waves propagate

## Slide 44: Point-to-Multipoint Links
Point-to-multipoint wireless link
  One transmitter communicates with several mobile clients
Maximize the signal distance by using an omnidirectional antenna at the central location
  Use directional, higher-gain antennas at the remote locations

## Slide 45
Figure 4-19 Point-to-multipoint links using a combination of omnidirectional
and directional antennas

## Slide 46: Point-to-Point Links
Point-to-point wireless link
  Connects two computer networks in different buildings
Directional antennas provide the most reliable method of transmitting RF waves
  Narrow beams and high gain ensure that most of the energy of the RF wave will be used
Telephone companies make extensive use of point-to-point microwave links (instead of cables)
  For long-distance voice and data communications
  Cost of maintaining a wireless link is lower than installing and maintaining cables

## Slide 47
Figure 4-20 Point-to-point link using directional antennas

## Slide 48: Fresnel Zone
RF waves have a tendency to spread out
  Space between two antennas would be more accurately represented by an ellipse
    Called the Fresnel zone
When planning a wireless link
  At least 60% of the Fresnel zone must be kept clear of obstructions
  May affect the height of the antenna tower

## Slide 49
Figure 4-21 Fresnel zone
Augustin-Jean Fresnel (French physicist): studied the polarization of light waves

## Slide 50: Link Budgets
Link budgets
  Calculate whether you will have enough signal strength to meet the receiver’s minimum requirements
A simple link budget equation looks like this:
  Received Power(dBm) = Transmitted Power(dBm)
  + Gains(dB) − Losses(dB)
Information needed to calculate link budget includes:
  Gain of the antennas
  Cable and connector losses for receiver and transmitter
  Free space loss figure, … etc

## Slide 51: Antenna Alignment
One of the challenges of implementing a point-to-point link:
  Positioning the antennas at the same height and point them toward one another
Some basic tools for antenna alignment:
  A compass to position the antenna in the correct direction
  A spotting scope or binoculars
  A means of communication, such as a walkie-talkie or a cellular phone
  If the distance is reasonably short, a light source, such as a flashlight or laser pointer

## Slide 52: Antenna Alignment
Spectrum analyzer
  Used for long distance and accurate antenna alignment
  Displays the signal amplitude and frequency
  Can also detect interference in a particular frequency or channel
Figure 4-22 Spectrum analyzer

## Slide 53: Other Challenges of Outdoor Links
Radio waves can reflect, diffract, or be absorbed by some materials
Weather phenomena can affect the performance and reliability of wireless links
  Examples: heavy fog, rain, dust, or snowstorms
Air disturbances and changes in temperature can also affect wireless links
Seasonal changes can impact a wireless link
  An antenna that was setup in winter (when there were no leaves on trees) may not work as well in the spring (when leaves can block a percentage of the Fresnel zone)

## Slide 54: Summary
Gain occurs when a signal is amplified or when most of the signal’s energy is focused in one direction
Loss occurs when the energy of a signal decreases
Decibel (dB) is a relative measurement
  Simplifies the calculations of gain and loss, and indicates the strength of a signal
An isotropic radiator is a theoretical perfect sphere that radiates power equally, in all directions
Most common type of antenna is a passive antenna

## Slide 55: Summary
Size of an antenna depends primarily on the frequency that it is designed to transmit or receive
Types of antennas: omnidirectional and directional
Free space loss is caused by the natural tendency of RF waves to spread out
Antennas have a horizontal and a vertical radiation pattern
Basic types of one-dimensional antennas
  Monopole
  Dipole

## Slide 56: Summary
Smart antennas can track a mobile user
  And send a narrower, more efficient beam
Special LMR antenna cables are used to reduce the signal loss
RF waves propagate differently depending on the frequency of the signal
Types of links: point-to-multipoint and point-to-point
Challenges of outdoor links
  Weather phenomena
  Seasonal changes

## Slide 57: Homework (Antenna)
เสาอากาศตัวส่ง มีค่ากำลังส่ง 250 mWatt มีค่ากำลังขยาย (Gain) 9 dB และ มีค่าลดทอนในสายสัญญาณ (Cable loss) 4 dB ค่า Free Space Path loss คิดเป็น 0.5 dB ต่อ 100 เมตร เสาอากาศฝั่งรับไม่มีการขยายสัญญาณ แต่มีค่าลดทอนสัญญาณในสายสัญญาณ 2 dB
จงคำนวณหากำลังของสัญญาณที่ฝั่งรับได้รับ หลังจากสัญญาณผ่านสายอากาศและสายสัญญาณฝั่งรับแล้วว่ามีขนาดกี่ Watt โดยใช้กฎ Ten & Three
กำหนดให้ฝั่งรับและฝั่งส่งมีระยะทางห่างกัน 400 เมตร