## Slide 1: Chapter 6 High rate wireless personal area networks
Reference: Jorge Olenewa, Guide to Wireless Communications, 3rd edition, ISBN-13: 9781111307318, 2013
© Cengage Learning 2014
Department of Computer Engineering, Faculty of Engineering Prince of Songkla University, Phuket Campus

## Slide 2: Objectives
Define a high rate wireless personal area network (HR WPAN)
List the different HR WPAN standards and their applications
Explain how WHDI, WiGig, WirelessHD
Outline the issues facing WPAN technologies
Describe the security features of each HR WPAN technology

## Slide 3: High Rate WPAN Standards
HR WPAN applications
  Connecting digital cameras to printers and kiosks
  Connecting laptops to multimedia projectors and sound systems
  Connecting camera-equipped cell phones and tablets to laptops and printers
  Connecting speakers in a surround system to amps and receivers
  Linking multiple display monitors
  And others

## Slide 4: High Rate WPAN Standards
Application characteristics
  Require high throughput; 20 Mbps or more
  Low-power transceivers, Low cost
  Require quality-of-service (QOS) capabilities
  Connections should be simple and automatic
  Security features should be included
  Internet access and use of digital TVs as wireless displays

## Slide 5: High Rate WPAN technologies
WirelessHD
  802.15.3c  7-25 Gbps  60 GHz
    www.wirelesshd.org
  WHDI  1.5 Gbps  5 GHz
    www.whdi.org
WiGig (www.wigig.org)
  802.11ac  7 Gbps  5 GHz
  802.11ad  7 Gbps  60 GHz
WLAN
  802.11n  600 Mbps  2.4 or 5 GHz
Notes: 60 GHz uses beamforming
5 GHz uses MIMO
WirelessHD is a standard of the WirelessHD Consortium. It uses the 60-GHz band but is not Wi-Fi compatible. In fact, it was designed from scratch to be used as a video transport method rather than using existing Wi-Fi or some other technology not optimized for video. It supports the 1080p/60-Hz video format with a 10–9-pixel error rate in addition to all EIA-861 video formats. It also supports both picture-in-picture (PI) and single source to multiple displays.
WirelessHD เน้น Audio/Video cable replacement โดยใช้ RF 60 GHz

## Slide 6: High Rate WPAN Standards
IEEE 802.15.3c
  WirelessHD Consortium created a spec based on this standard for combining the transmission of HD video, multichannel audio, and data for multimedia streaming in the 60 GHz band

## Slide 7: Networking Audio, Video, and Other I/O Devices
Wireless Home Digital Interface (WHDI)
  Developed primarily for delivery of uncompressed video and audio with cable-connection quality
  Used to mirror screens of multiple devices
  Works in 5 GHz frequency band; coexists with 802.11a and 802.11n and cordless phones
  Max range of 100 ft.
  No special adapters needed; supports HDMI

## Slide 8: Networking Audio, Video, and Other I/O Devices
Wireless Gigabit (WiGig) Architecture
  Designed for 802.11n and 802.11ac compatibility; will support 802.11ad in 60 GHz band
  WiGig uses beamforming to maintain reliable connections at higher frequencies
  Supports two modulation types in 60 GHz band:
    Single-carrier modulation
    Orthogonal frequency-division multiplexing (OFDM)
Notes: Single carrier modulation (max: pi/2-16QAM at 4 Gbps)
OFDM (max: 64QAM at 7 Gbps)
AV display standard support เช่น HDMI, I/O (USB , PCIe) at the PHY and MAC layer, bypassing higher-layer WLAN (TCP/IP)

## Slide 9: Networking Audio, Video, and Other I/O Devices
WirelessHD and IEEE 802.15.3c
  Consumer products already available
  802.15.3c amendment only refers to 60 GHz band
  Supports devices transmitting at different speeds to allow mobile devices to conserver battery power
  Table 6-1 shows speeds and applications supported by WirelessHD

## Slide 10
Table 6-1 Speeds supported in WirelessHD

## Slide 11: Networking Audio, Video, and Other I/O Devices
WirelessHD and IEEE 802.15.3c
  Source device: transmitter
  Sink device: receiver
  Divides PHY layer into three sections:
    Low-Rate PHY (LRP) – data rates 2.5 to 40 Mbps
    High-Rate PHY (HRP) – data rates to 7 Gbps and up to 25 Gbps using spatial multiplexing
    High-or-Medium-Rate PHY (HMRP) – data rates of 476 Mbps to 2 Gbps
  Also supports USB 2.0, 3.0 and HDMI
  Uses beamforming for line-of-sight/non-line-of-sight transmissions
Notes: Spatial multiplexing = a technique that divides the data frame into multiple parts and transmits each part of the same data frame using a separate radio and antenna,
Effectively increasing the transmission rate by sending the data in parallel.

## Slide 12
Figure 6-3 Recommended WirelessHD protocol-layer implementation
Notes: There are four functional divisions in the WirelessHD layering model; the PHY layer, the
MAC sublayer, the Adaptation sublayer and the Station Management Entity (SME). The
relationships of the various parts is illustrated in Figure 6-3. There are two protocols in the
adaptation sublayer; the AVC protocol and the A/V packetizer. The AVC protocol
performs the device control, the connection control, the device capability and so on. The
role of A/V packetizer is to make the formatted A/V data for the HMRP data service.
The four entities provide three types of service: high rate data service, low rate data
service, and the management service. The high data rate service supports video, audio
and data delivery. The low data rate service supports audio data, MAC commands, and
small amounts of asynchronous data. The layering model is defined in the specification
only to describe the functionality of the WirelessHD system.
10 Audio video control (AV/C) specification
10.1 Overview
The AV/C includes the following functions;
· Device capability exchange – In this function, a device discovers other devices
and exchanges device information (e.g. device category, device name) with other
devices.
· Connection control – In this function, a device establishes or releases the AV
stream connection between a Source and a Sink by using AVC messages.
· Device control – In this function, a device controls other device by using AVC
messages (e.g. power on/off, play/stop etc.).

## Slide 13
Figure 6-2 Beamforming

## Slide 14: WirelessHD and 802.15.3 MAC layer
Devices associate with the piconet coordinator (PNC)
  PNCs are usually a sink device such as HD TV
  Coordinator acts as a station on the wireless video area network (WVAN)
  The first sink devices assumes the role of PNC
  PNC responsible for QoS

## Slide 15: WirelessHD and 802.15.3 MAC layer
Piconet coordinator (PNC)
  Role assumed by the first device in the area
  Provides all of the basic communications timing in a piconet
  PNC sends a beacon
The piconet is peer-to-peer
  Devices can transmit data directly to each other
The PNC is also responsible for managing QoS
Devices can form a dependent piconet

## Slide 16
Figure 6-4 Wireless video area network (WVAN) topology example
Notes: The WVAN consists of one Coordinator and zero or more Stations. The Coordinator is
normally, but not always, a device that is a sink for audio or video data, e.g., a display,
but also potentially a media storage device like a PVR. A Station, on the other hand, is a
device that has media that it can source and/or sink or has data to exchange, potentially at
the same time. The device that is the Coordinator also acts as a Station in the WVAN.
An example of a WVAN is illustrated in Figure 6-4.
The high-rate PHY (HRP) and medium-rate PHY (MRP) support multi-Gb/s throughput
at distance of 10 m through adaptive antenna technology. Because of this, the high-rate or
medium-rate PHY (HMRP) is highly directional and can only be used for unicast
connections. The HMRP is optimized for the delivery of uncompressed high definition
video, other data can be communicated using the HMRP. To support multiple video
resolutions, the HMRP has more than one data rate defined. The HMRP carries:
· isochronous data such as audio and video,
· asynchronous data,
· MAC commands,
· antenna steering information, and
· higher layer control data for A/V devices.
The low-rate PHY (LRP) is a multi-Mb/s bidirectional link that also provides a range of
10 m. Multiple data rates are defined for the LRP, with the lower data rates having near
omni-directional coverage while the highest data rates are directional. Because the LRP
has near omni-directional modes, it can be used for both unicast and broadcast
connections. Furthermore, because all Stations support the LRP, it can be used for
Station-to-Station links. The LRP supports multiple data rates, including directional
modes, and is used to carry:
· low-rate isochronous data such as audio,
· low-rate asynchronous data,
· MAC commands including the beacon,
· acknowledgements for HMRP packets,
· antenna beam forming information,
· capabilities information, and
· higher layer control data for A/V devices.
The HMRP and LRP operate in overlapping frequency bands and so they are coordinated
in a TDMA manner by the MAC.

## Slide 17
Figure 6-5 802.15.3 piconet topology

## Slide 18: WirelessHD and 802.15.3 MAC layer
Two types of dependent piconets – dependent on the PNC of another (parent) piconet
  Child piconets
    Has its own piconet ID but child PNC is a member of the original (parent) piconet
  Neighbor piconets
    Separate piconet but depends on original piconet’s PNC to allocate time for transmitting

## Slide 19
Figure 6-6 Child piconet

## Slide 20
Figure 6-7 Neighbor piconet

## Slide 21: WirelessHD and 802.15.3 MAC layer
Figure 6-9 General MAC frame format
Notes: Frame control = protocol version, type of frame, encrypt status, how receiving device should acknowledge it, end frame or data follow?
Piconet id = หมายเลข piconet network, node will receiving frames by the same piconet id.
Index is used for managing and uniquely identifying different asynchronous and isochronous streams.

## Slide 22: WirelessHD and 802.15.3 MAC layer
The IEEE 802.15.3 MAC layer designed to support these features:
  Connection time (association) is fast
  Devices associated with the piconet can use a short, one-octet device ID
  Devices can obtain information about the capabilities of other devices
  Peer-to-peer (ad hoc) networking
  Data transport with QoS
  Security
  Efficient data transfer using superframes (Figure 6-8)

## Slide 23
Figure 6-8 802.15.3 superframe

## Slide 24: WirelessHD and 802.15.3 MAC layer
IEEE 802.15.3 superframe structure
  A beacon – used to set time allocations and communicate management information
  An optional contention access period (CAP) – used for association, command communication, or asynchronous data
  The channel time allocation period (CTAP) – includes channel time allocations (CTA) and may include management channel time allocation (MCTA) periods

## Slide 25: WirelessHD and 802.15.3 MAC layer
Communication in an 802.15.3 piconet
  Beacon frame sent by the PNC includes a variable indicating the end of the CAP
  Devices can send asynchronous data in the CAP
  Devices can request channel time on a regular basis
    Requested channel time is called isochronous time
  Devices can also request channel time for asynchronous communications in the CTAP
    Communications use a time division multiple access (TDMA) scheme

## Slide 26: WirelessHD and 802.15.3 MAC layer
Power management
  802.15.3 power-saving methods
    Device synchronized power save (DSPS) mode
    Piconet synchronized power save (PSPS) mode
    Asynchronous power save (APS) mode
  Wake superframe
    Superframe designated by the PNC
    Devices that are in power save mode wake up and listen for frames addressed to them

## Slide 27: DSPS mode Device Synchronoized Power Save
Allows devices to sleep for the duration of several superframes
Be able to wake up in the middle of a superframe to transmit or receive data
Other devices in the piconet are informed about which devices in a group (called DSPS set) in this mode when they will awake and can receive/ transmit data

## Slide 28: PSPS mode Piconet Synchronoized Power Save
Allows devices to sleep during intervals defined by the PNC
PNC selects beacons to serve as system-wide wake beacons and indicates the next one to occur in the beacon fields
All devices in PSPS mode are required to wake up and listen to the wake beacons

## Slide 29: APS mode Asynchronous Power Save
Allow devices to sleep for long periods of time until they choose to wake up and listen to a beacon
A device in APS mode must communicate with the PNC before the end of its association time-out period (ATP)
  To maintain its membership in the piconet

## Slide 30
Figure 6-10 Wake beacons

## Slide 31: 802.15.3c PHY Layer
Uses 60 GHz band and supports the channel plan
  Four 2 GHz wide channels
  Channel aggregation is supported
Table 6-2 channel plan

## Slide 32: 802.15.3c PHY Layer
Contains a number of optional enhancements
  Passive scanning
    Channel scanning
  Channel energy detection
    Frequency and signal strength detection before joining a piconet
  Channel quality requests
  Link quality indication
    Request channel/link quality
  Transmit power control
    Increase/decrease power to improve link quality

## Slide 33: 802.15.3c PHY Layer (Cond’t)
Contains a number of optional enhancements
  Neighbor and child piconets
  Two superframe transmission modes
    When using omnidirectional transmission, the superframe is sent only once to all stations
    When using beamforming, the superframe is transmitted multiple times in the direction of each station (round-robin fashion)
  Max data frame length of 8,388,608 octets
    Maximize throughput

## Slide 34: 802.15.3c PHY Layer
Modulation
  Variations of BPSK and QPSK
  Required to transmit headers using LRP
  Single carrier for LRP and OFDM encoding for HRP and MRP

## Slide 35: Frequency Division Multiple Access (FDMA)
Old conventional method (Analog TV, Radio etc.)
Use separate carrier frequency for individual transmission
Radio frequency
fｃ１
fｃ2
fｃ3
fｃN
Carrier frequency
Occupied BW
Channel separation
Guard band

## Slide 36: Spectrum comparison for same data rate transmission
frequency
Single carrier
frequency
OFDM
frequency
Multi carrier
Notes: Old fashion Broadband use wideband of single carrier,
OFDM uses multiple carriers (as wide as wide single carrier) :
OFDM gets high speed serial data, sperates it to multiple channels (with multiple carriers)
(also insert cyclic prefix to prevent ISI (multipath distrotion + reduce error) and send multiple carriers to a receiver,
A receiver gets mutliple carriers (which are orthogonal) and convert to serial

## Slide 37: Actual OFDM spectrum
Amplitude
Frequency
Multi-carrier Amplitude modulation scheme
Each Carrier’s amplitude is modulated
Well-suited for Wireless Communication
No interference on the center of each carrier
Notes: OFDM advantages:
- use effective bandwidth (overlap frequency band)
- use with large number of modulation (e.g. 4096-QAM) because of non-overlap channels + slower data rate (with parellel sending – less error)
- errors affected only a narrow band carrier (with wide band, errors affected to whole frequency band (faster rate)
Disadvantage:
- solves multiplath distrotion problem with guard time (cyclic prefix)

## Slide 38: Mesh Networking (802.15.5)
Mesh networking
  Each device connects to all other devices within range
  Effectively creating multiple paths for transmission
  Enable WPANs to cover an entire building

## Slide 39
Figure 6-11 Mesh network

## Slide 40: WPAN Challenges
Challenges
  Competition Among WPAN Standards
  WPAN Security
  Security for IEEE 802.15.3 HR WPANs
  Cost of WPAN Components
  Industry Support for WPAN Technologies
  Protocol Functionality Limitations
  Spectrum Conflict

## Slide 41: Competition Among WPAN Standards
IEEE 802.15.1 and 802.15.3 are positioned to compete with Bluetooth for market share
  It will take a few years before 802.15.3 products begin to ship in volume
WirelessHD, WiGig, and WHDI have the potential to quickly outpace Bluetooth

## Slide 42: WPAN Security
IEEE 802.15.3 HR WPAN security
  Based on Advanced Encryption Standard (AES)
  Uses a 128-bit key
  Two security modes:
    Mode 0: does not encrypt or protect the data
    Mode 1: strong cryptography based on AES

## Slide 43: Cost of WPAN Components
Bluetooth currently supports more devices than other WPAN technologies
  Industry experts believe that price must be reduced to reach competitive advantage
Does not make economic sense to use a chip that costs $5 to replace a higher-data rate cable that costs < $10
Notes: Bluetooth is expensive for the beginning, and about $5 presently (that’s a reason why bluetooth wins the game)
bluetooth $5 replace higher data rate cable < $10,
if wirelessHD is cheap and has data rate equal or greater than cable,
the replacing is possible.

## Slide 44: Industry Support for WPAN Technologies
Industry experts predict that new technologies will be more quickly embraced by manufacturers
  Such as WirelessHD and ZigBee

## Slide 45: Protocol Functionality Limitations
Bluetooth protocol suffers from its lack of hand-off capability between piconets
Hand-off
  Ability to move from one master or PNC to another
    Without getting disconnected from the network
ZigBee and WirelessHD have the advantage over Bluetooth in this area

## Slide 46: Summary
HR WPANs are optimized for multimedia transmissions
  Optimized for multimedia voice and video signals
WHDI defines wireless connectivity using the 5 GHz band
WiGig defined a set of specs that include protocol adaptation layers to support wireless HDMI, USB, PCIe, data, video, and audio

## Slide 47: Summary
The 60 GHz band can only support short-range connections
WiGig supports the same modulation and coding schemes in the ISM and U-NII bands as 802.11
WirelessHD is the only spec that uses IEEE 802.15.3c standard
WirelessHD defines three PHY layers: LRP, HRP, and MRP

## Slide 48: Summary
WiGig and WirelessHD support beamforming
802.15.3c supports peer-to-peer networking
Efficient data transmission is accomplished using a superframe
Devices can send asynchronous data in the CAP or request channel time for async during CTAP
802.15.3 devices support three power-saving modes: DSPS, PSPS, and APS

## Slide 49: Summary
Challenges for WPANs include speed, security, cost, industry support, interference, and protocol limitations
WPAN devices that are designed to be small and consume very little power have limited processing capabilities and storage