## Slide 1: Chapter 10 Wireless WIDE Area Networks
Reference: Jorge Olenewa, Guide to Wireless Communications, 3rd edition, ISBN-13: 9781111307318, 2013
© Cengage Learning 2014
Department of Computer Engineering, Faculty of Engineering Prince of Songkla University, Phuket Campus

## Slide 2: Objectives
Describe wireless wide area networks (WWANs) and how they are used
List the types of applications that can be used on a digital cellular phone
Explain the basic concepts of how cellular telephony functions
Describes the various generations of cellular telephony
Discuss satellites and their applications in WWANs

## Slide 3: Cellular Telephone Technology
Digital cellular telephones can be used to:
  Browse the Internet
  Send and receive short messages and e-mails
  Participate in videoconferencing
  Receive various sorts of information
  Run a variety of business applications
  Connect to corporate networks
  Watch television or on-demand movies
  Take and transmit pictures and short movies
  Locate family members and employees using GPS

## Slide 4: Cellular Telephone Technology
Short Message Services (SMS)
  One of the most widely used applications
  Allows for the delivery of short, text-based messages between cellular phones
    Messages are limited to 160 characters
  Applications
    Person-to-person
    Agent-to-person
    Information broadcast services
    Software configuration
    Advertising

## Slide 5: How Cellular Telephony Works
Keys to cellular telephone networks
  Cells
    Typical cell ranges from a few thousand feet (diameter) to approximately 10 square miles (26 square meters)
    Cells may vary in radius from 1 to 30 kilometers
    At the center of each cell is a cell transmitter connected to a base station
    Each base station is connected to a mobile telecommunications switching office (MTSO)
      Link between the cellular network and the wired telephone world
      Controls all transmitters and base stations
Notes: Cells may vary in radius from 1 to 30 kilometres (0.62 to 18.64 mi). The boundaries of the cells can also overlap between adjacent cells and large cells can be divided into smaller cells.

## Slide 6
Figure 10-1 Cellular phone network

## Slide 7: How Cellular Telephony Works
Keys to cellular telephone networks (cont’d)
  Transmitters and cell phones operate at low power
    Enables the signal to stay confined to the cell
    Signal at a specific frequency does not go far beyond the cell area
      Same frequency can be used in other cells at the same time
      Except in adjacent cells

## Slide 8
Figure 10-2 Frequency reuse with three frequencies

## Slide 9: How Cellular Telephony Works
Cell phones have special codes
  Codes are used to identify the phone, phone’s owner, and carrier or service provider (e.g., AIS, DTAC, TRUE)
Some cellular phones require a SIM card to be installed before they can be used

## Slide 10: How Cellular Telephony Works
SIM (subscriber identity module) card – very small electronic card used to associate the phone with the user’s account and with the carrier
SIM cards have:
  ROM between 64 KB and 512 KB
  RAM between 1 KB and 8 KB
  EEPROM between 64 KB and 512 KB
Users can move the card between one phone and another and use different phones without reprogramming
Notes: SIM cards are like micro-computers and contain many of the same elements or components that one would find in a computer or PDA. SIM cards are composed of a CPU (Central Processing Unit) to execute programs and commands, a ROM unit for "program memory," a RAM unit for "working memory," an EPROM for "data memory" and a "Serial communication module" for communicating with the cell service provider's network. Read more : http://www.ehow.com/how-does_5369478_sim-cards-work.html
More: https://www.defcon.org/images/defcon-21/dc-21-presentations/Koscher-Butler/DEFCON-21-Koscher-Butler-The-Secret-Life-of-SIM-Cards-Updated.pdf

## Slide 11
Table 10-1 Cellular phone codes
Notes: SID = ISP (sent from ISP and store in SIM card)
ESN (CDMA phone) = IMEI (GSM) = phone serial number
IMSI = MCC + MNC + MIN
MCC = Country code
MNC = Network code (local area code)
MIN = phone number

## Slide 12: How Cellular Telephony Works
When user moves within the same cell
  Transmitter and base station for that cell handle all of the transmissions
As the user moves toward the next cell
  A handoff process occurs
Roaming
  User moves from one cellular network to another

## Slide 13
Figure 10-4 Handoff and roaming

## Slide 14: How Cellular Telephony Works
Steps to receive a call
  Cell phone listens for the SID being transmitted by the base station on the control channel
  Phone compares SID with its programmed SID
    If they match, phone is in a network owned by carrier
  If SIDs do not match, phone is roaming
  When a call comes in, MTSO locates the phone through the registration request
  User can move to another cell
  Phone and transmitter can change frequencies as required

## Slide 15
Figure 10-5 Receiving a call on a cellular phone

## Slide 16: Evolution of Cellular Telephony
Cellular phones have been available since the early 1980s in the United States
Most industry experts outline several generations of cellular telephony

## Slide 17: Cellular Network Generations
It is useful to think of cellular Network/telephony in terms of generations:
  0G: Briefcase-size mobile radio telephones
  1G: Analog cellular telephony
  2G: Digital cellular telephony
  3G: High-speed digital cellular telephony (including video telephony)
  4G: IP-based “anytime, anywhere” voice, data, and multimedia telephony at faster data rates than 3G (2012–2015)
  5G: Super fast/efficient Mobile network (converged fiber, 2020)
From: ftp://ftp.kemt.fei.tuke.sk/MobilneKomunikacie/ _materialy/Podklady/10_IPv6_summit.ppt

## Slide 18: First Generation Cellular Telephony
First Generation (1G)
  Uses analog signals modulated using FM
  Based on Advanced Mobile Phone Service (AMPS)
    Operates in the 800-900 MHz frequency spectrum
    Each channel is 30 KHz wide with a 45 KHz passband
    There are 832 frequencies available
    Uses Frequency Division Multiple Access (FDMA)
    FDMA allocates a single cellular channel with two frequencies to one user at a time
1G networks use circuit-switching technology
http://www.cntr.salford.ac.uk/comms/etacs_mobiles.php

## Slide 19
Figure 10-6 FDMA

## Slide 20: First Generation Cellular Telephony
Circuit-switching technology
  Makes a dedicated and direct physical connection
    Between the caller and the recipient
Analog signals are prone to interference
  Do not have the same quality as digital signals

## Slide 21: Second Generation Cellular Telephony
Second Generation (2G)
  Transmits data between 9.6 Kbps and 14.4 Kbps
    In the 800 MHz and 1.9 GHz frequencies
  2G networks are also circuit-switching
  2G systems use digital transmissions
Digital transmissions
  Use the frequency spectrum more efficiently
  Over long distances, the quality of the voice transmission does not degrade
  Difficult to decode and offer better security

## Slide 22: Second Generation Cellular Telephony
Digital transmissions (cont’d)
  Use less transmitter power
  Enable smaller and less expensive individual receivers and transmitters
Multiple access technologies
  Time Division Multiple Access (TDMA)
  Code Division Multiple Access (CDMA)
  Global System for Mobile communications (GSM)
    Uses a combination of FDMA and TDMA technologies

## Slide 23
Figure 10-7 TDMA

## Slide 24
Figure 10-8 CDMA

## Slide 25: 2.5 Generation Cellular Telephony
2.5 Generation (2.5G)
  Interim step between 2G and 3G
  Operates at a maximum speed of 384 Kbps
  Primary difference between 2G and 2.5G:
    2.5G networks are packet-switched
  Advantages of packet switching
    Much more efficient
      Can handle more transmissions over a given channel
    Permits an always-on connection

## Slide 26: 2.5 Generation Cellular Telephony
Three 2.5G network technologies
  General Packet Radio Service (GPRS)
    For TDMA or GSM 2G networks
    Uses eight time slots in a 200 KHz spectrum and four different coding techniques to transmit at 114 Kbps
  Enhanced Data rates for GSM Evolution (EDGE)
    Can transmit up to 384 Kbps
    Based on a modulation technique called 8-PSK
  CDMA2000 1xRTT (1-times Radio Transmission Technology)
    Operates on two 1.25 MHz-wide frequency channels
    Supports 144 Kbps packet data transmission

## Slide 27: Third Generation Cellular Telephony
Third Generation (3G)
  Intended to be a uniform and global standard for cellular wireless communication
Standard data rates
  144 Kbps for a mobile user
  386 Kbps for a slowly moving user
  2 Mbps for a stationary user
3G network technologies
  CDMA2000 1xEVDO
    For 2.5G CDMA2000 1xRTT networks

## Slide 28: Third Generation Cellular Telephony
3G network technologies (cont’d)
  CDMA2000 1xEVDV is the successor of CDMA2000 1xEVDO
  Wideband CDMA (W-CDMA)
    For 2.5G EDGE networks
  High-Speed Downlink Packet Access (HSDPA)
    Beyond W-CDMA
    Uses a 5 MHz W-CDMA channel, variety of adaptive modulation, multiple in multiple out (MIMO) antennas, and hybrid automatic repeat request (HARQ)

## Slide 29: Third Generation Cellular Telephony
3G network technologies (cont’d)
  HSPA+ (also called Evolved HSPA) – successor to HSDPA
    Provides theoretical data rates up to 168 Mbps on the downlink and 22 Mbps on the uplink
    Provides an upgrade path to latest-generation technology: LTE (Long Term Evolution)
  LTE (also known as 4G)
    LTE Advanced: expands on LTE by allowing carriers to combine up to five 20-MHz-wide frequency channels
    Maximum downlink data rate: up to 1 Gbps
Notes: HSPA+: IP4, IP4S, S3
4G LTE:
IP5, IP5S, IP5C, IP6Plus
SS Note 3, S4, S5

## Slide 30
Figure 10-9 Cellular technology migration paths

## Slide 31
Table 10-2 Digital cellular technologies

## Slide 32
Figure 10-10 Comparison of data-rate speeds for various cellular technologies

## Slide 33: Limited Spectrum
Spectrum
  Single largest factor limiting the development of 3G
Although 3G and 4G can operate at almost any spectrum
  Industry tries to use the same part of the spectrum for communications around the world
    1.710 to 1.855 GHz and 2.520 to 2.670 GHz
In North America, the 700 MHz band (formerly used for analog television), is also being used for cellular networks

## Slide 34: Costs
Monthly service fees for data transmission can be expensive
User cost for cellular phone service pales in comparison to costs for the carriers to build and constantly upgrade cellular networks
  In 2001, Germany paid over $46 billion for licenses to use the spectrum

## Slide 35: Satellite Broadband Wireless
Use of satellites for personal wireless communication is fairly recent
Satellite use falls into three broad categories
  Satellites are used to acquire scientific data and perform research in space
  Satellites look at Earth from space
  Satellites are used as reflectors that bounce or relay signals from one point on Earth to another
    Wireless communications falls under this use of satellites

## Slide 36
Figure 10-11 Three types of satellites

## Slide 37: Satellite Transmissions
Satellites generally send and receive on one of four frequency bands
Frequency band affects the size of the antenna
Table 10-3 Satellite frequencies

## Slide 38
Figure 10-12 Satellite antenna sizes

## Slide 39: Satellite Transmissions
Class and Type of Service
  Satellites can provide two classes of service
    Consumer class service
      Shares the available bandwidth between the users
    Business class service
      Offers dedicated channels with dedicated bandwidth
      More expensive
  Types of connectivity
    Point-to-point, point-to-multipoint, and multipoint-to-multipoint

## Slide 40
Figure 10-13 Types of satellite service

## Slide 41: Satellite Transmissions
Modulation techniques
  Binary phase shift keying (BPSK) – Shifts the starting point of a carrier wave by 180 degrees
  Quadrature phase shift keying (QPSK) – Shifts the starting point of the carrier wave by 90 degrees
  Eight-phase shift keying (8-PSK) – Can transmit up to 3 bits per symbol
  16-level quadrature amplitude modulation (16-QAM) – Primarily used for sending data downstream; considered efficient but is susceptible to interference

## Slide 42: Satellite Classification
Satellite systems are classified according to the type of orbit they use
Three orbits:
  Low earth orbit (LEO)
  Medium earth orbit (MEO)
  High earth orbit (HEO)
    Most HEO satellites fall into a subclass called geosynchronous earth orbit (GEO)

## Slide 43: Low Earth Orbit (LEO)
Low earth orbit (LEO) satellites
  Circle the Earth at altitudes between 200 to 900 miles
  Must travel at high speeds
    So that the Earth’s gravity will not pull them back into the atmosphere
  Area of Earth coverage (called the footprint) is small
LEO systems have a low latency
  Use low-powered terrestrial devices (RF transmitters)
  Round trip time: 20 to 40 milliseconds for a signal to bounce from an Earth-bound station to a LEO, then back to an Earth station

## Slide 44
Figure 10-14 LEO footprint

## Slide 45: Low Earth Orbit (LEO)
LEO satellites groups
  Little LEOs
    Frequencies below 1 GHz
    5MHz of bandwidth, Data rates up to 10 kbps
    Provides pager, satellite telephone, and location services
  Big LEOs
    Frequencies above 1 GHz
    Support data rates up to a few mbps
    Carries voice and data broadband services, such as wireless Internet access
In the future, LEOs are expected to be in demand for three markets:
  Rural conventional telephone, global mobile digital cellular, and international broadband services

## Slide 46: Medium Earth Orbit (MEO)
Medium earth orbit (MEO) satellites
  Orbit the Earth at altitudes between 1,500 and 10,000 miles
  Some MEO satellites orbit in near-perfect circles
    Have a constant altitude and constant speed
  Other MEO satellites revolve in elongated orbits called highly elliptical orbits (HEOs)
Advantages
  MEOs do not have to travel as fast; a MEO can circle the Earth in up to 12 hours
  Have a bigger Earth footprint

## Slide 47
Figure 10-15 MEO footprint

## Slide 48: Medium Earth Orbit (MEO)
MEO Disadvantage
  Higher orbit increases the latency
  Round trip time: 50 to 150 milliseconds
HEO satellites (High Earth Orbit)
  Have a high apogee (maximum altitude) and a low perigee (minimum altitude)
  Can provide good coverage in extreme latitudes
  Orbits typically have a 24-hour period

## Slide 49: Geosynchronous Earth Orbit (GEO)
Geosynchronous earth orbit (GEO) satellites
  Stationed at an altitude of 22,282 miles (35,860 km)
  Orbit matches the rotation of the Earth
    And moves as the Earth moves
  Can provide continuous service to a very large footprint
    Three GEO satellites are needed to cover the Earth
  Have high latencies of about 250 milliseconds
  Require high-powered terrestrial transmitting devices

## Slide 50
Figure 10-16 Three GEO satellites covering the entire planet

## Slide 51
Table 10-4 Satellite orbit advantages and disadvantages

## Slide 52: Satellite orbits
 | Distance (km) | Period
Low Earth Orbit (LEO) | 700 - 2000 | ~2 hr
Medium Earth Orbit (MEO) | 10,000 – 15,000 | 6-12 hr
Geosynchronous Earth Orbit (GEO) | 36,000 | 24 hr
From: Omer, Satellite Networks Research Laboratory (SATLAB)

## Slide 53: Satellite Technology Outlook
Satellites can provide wireless communication
  In areas not covered by cellular or WiMAX
Satellites today are enabling carriers to offer
  Internet access and voice calls to passengers and crews across large oceans
    And in high latitudes and remote corners of the Earth
Can also make these services available in many other unpopulated areas

## Slide 54: Summary
In cellular telephone networks, the coverage area is divided into sections called cells
Some cellular phones use SIM cards to store user and carrier information
First Generation (1G) cellular technology uses analog signals and a circuit-switching technology to transmit data at a maximum speed of 9.6 Kbps
Second Generation (2G) can transmit data between 9.6-14.4 Kbps using digital signals instead of analog signals

## Slide 55: Summary
2.5G networks transmit data at a maximum speed of 384 Kbps and uses a packet-switched technique
3G networks provide new and expanded capabilities and data applications features to mobile users
4G networks achieve data rates comparable to wired networks
  Long Term Evolution (LTE) technology
One of the most widely used applications in the world today is Short Message Services (SMS)
  Allows for delivery of short, text-based messages

## Slide 56: Summary
Satellites used for wireless data connectivity
  Employ common modulation and multiplexing techniques
Satellite orbit types
  LEO satellites
  MEO satellites
  GEO satellites